## Slide 1: EE 2361: Introduction to Microcontrollers
Peng Li
lipeng@umn.edu
06/26/2015

## Slide 2: Topics
Review t1_first.c
Timer Delay Computation
Timer’s Range vs Resolution
Timer’s Interrupt
Using Loops to generate long delay
Disassmebly

## Slide 3: Compute Delay
Instruction Frequency | PR1 | Prescale | Delay
16MHz | 5000 | 1 | 0.3125 ms
16MHz | 100 | 8 | 50 us
16MHz | 50000 | 256 | 0.8 s

## Slide 4: Exercise
1. Compute the value of PR1 and Prescale for a 200ms delay (the instruction frequency is 16MHz).
2. What is the maximum delay that can be generated using the timer?

## Slide 5: Timer’s Resolution
The minimum delay of the timer:
Prescalar / Clock Frequency
Prescalar (16MHz Frequency) | Timer Resolution
1 | 0.0625us
8 | 0.5us
64 | 4us
256 | 32us

## Slide 6: Timer’s Range
The maximum delay of the timer.
Max PR1 * Prescalar / Clock Frequency
Prescalar (16MHz Frequency) | Timer Range
1 | 4.096ms
8 | 32.77ms
64 | 262.1ms
256 | 1.049s

## Slide 7: Exercise
Compute the value of PR1 and Prescale for a 200.008ms delay (the instruction frequency is 16MHz).

## Slide 8: Timer Interrupt
Page 125 of datasheet

## Slide 9: Long Delay
What if we want to generate a delay longer than 1 second?
t1_oneMin.c

## Slide 10: Disassembly
Window->Debugging->Output->Disassembly List File

## Slide 11: Exercise
A key is connected to RA0, write a program to measure how long the key has been pressed before it is released.

## Slide 12: Exercise
Same question. But what if the key has been pressed for a very long time?

## Slide 13: Reading Assignment
Kia’s video: https://www.youtube.com/watch?v=Btc1Bf4_Z_E