## Slide 1: EE 2361: Introduction to Microcontrollers
Peng Li
lipeng@umn.edu
06/29/2015

## Slide 2: Topics
t1_measureKeyPressDelay_ms.c
Timer based on T1CK.
Timer 2 & 3.
How to measure the delay of a function.
Interupt.

## Slide 3: T1CK
Page 125 of datasheet

## Slide 4: Example
t1_countT1CK.c
MPLAB Stimulus Window->Simulator->Stimulus Select Clock Stimulus Select T1CK under Pin
Measure the program runtime when you change the T1CK frequency (1, 2, 5, 10, 100)

## Slide 5: Timer 2/3
Can be used as a single 32-bit timer
Or two independent 16-bit timers
The same structure as timer 1
Read the block diagram on page 128 of datasheet, figure 12-1.

## Slide 6: Delay Measurement using Timer
t1_countNumInsSinX.c
We can also measure the delay using Stopwatch (Note that not every IDE has this tool).
Using Interrupt to measure delay with timer.

## Slide 7: Interrupt
What is an interrupt?
Doing my homework
Text message
Receive
Response
Another example is your laptop, think about how the CPU communicates with the disk, keyboard, and mouse.

## Slide 8: Interrupt Priorities
Doing my homework
Text message
Phone Call
Fire alarm

## Slide 9: Timer Priority Setup
Question: what is the default priority level for timer 1 and 2?

## Slide 10: CPU Priority Setup
Question: what is the default priority level for CPU?

## Slide 11: Interrupt Initialization
Example: int_first_t1.c
Section 7.4 of Datasheet (Page 93)
IPC Register (Interrupt Priority)
IFS Register (Interrupt Flag)
IEC Register (Interrupt Enable)
Page 68-92 of datasheet for details.

## Slide 12: IRS (Interrupt Service Routine)
Clear Interrupt Flag (IFS Register) What if we don’t clear it?
Run the service, such as do some computation.
If ISR is coded in assembly, it must be terminated using a RETFIE instruction to unstack the saved PC value, SRL value, and old CPU priority level. (Read Page 365 of programmer manual for details about this instruction)

## Slide 13: Reading Assignment
https://en.wikipedia.org/wiki/Interrupt
Section 7.0 of datasheet (Page 61).