## Slide 1: EE 2361: Introduction to Microcontrollers
Peng Li
lipeng@umn.edu
07/01/2015

## Slide 2: Topics
Interrupt Examples
Input Capture

## Slide 3: Example 1
t1_INT0_rangeVsResolution.c
Question 1: what does this code do?
Question 2: are we doing polling or interrupt?
Question 3: change pre-scalar to 1, and use stimulus to set Low Cycles to 16 and High Cycles to 35, what value did you read from TMR1, and why is that?

## Slide 4: Example 2
int_int0PinT1_determineDutyCycle.c
Question 1: what does this code do?
Question 2: are we doing polling or interrupt?
Question 3: use stimulus to set Low Cycles to 16 and High Cycles to 35, what value did you read from numCycles, and why is that?
Question 4: how can we change this code to a frequency counter?

## Slide 5: Example 3
int_t1T2_isFreqAboveX.c
The goal is to turn RB2 1 if the frequency on T1CK input is above a certain threshold PULSE_COUNT_THRESHOLD between two T2 interrupts.
T1 is setup to give interrupt every two pulses are seen on T1CK. So the number in PULSE_COUNT_THRESHOLD should be half the number of expected pulses between T2 interrupts.
T2 is setup to give interrupts every 1ms.
Is there anything wrong with this code? (hint: interrupt priority)

## Slide 6: Example 4
int_testIfHiPriIntDoesIntLowPriISR.c
This program sets the stage to test if higher priority interrupts actually do interrupt the interrupt service routine of lower priority interrupts.
We setup T1 and T2 to the same period, but create a phase difference so that T2 always happens a few cycles after T1.

## Slide 7: Input Capture
This module is used to capture a timer value from an independent timer based upon an event (rising/falling edge, or both) on the input pin.
It will need to work with timer 2 or 3.
It is very useful for applications requiring frequency (or time period) and pulse measurement.
  Frequency Counter
  Digital Oscilloscope
  Pulse Oximeter
  PS/2 Interface

## Slide 8: Input Capture Block Diagram
Page 133 of datasheet

## Slide 9: How to Configure ICx Pin
Tabel 10-2 (Page 108 of datasheet)
Register 10-5 (Page 113 of datasheet)

## Slide 10: ICxCON Register
Important Bits:
ICTMR
ICI
ICM
Page 134 of datasheet for details.

## Slide 11: Example
Measure the duty cycle of an external signal. Set RB0 to ‘1’ is the duty cycle is greater than 50%. (ic_dutyCycle.c)

## Slide 12: Reading Assignment
PIC24F Family Reference Manual Section 34. Input Capture with Dedicated Timer (Advance Information, posted on Moodle site)
Chapter 11 of “Programming 16-bit PIC Microcontrollers in C” 2nd Edition, by Lucio Di Jasio.