## Slide 1: EE 2361: Introduction to Microcontrollers
Peng Li
lipeng@umn.edu
07/08/2015

## Slide 2: Topics
Review Input Capture
Output Compare

## Slide 3: Input Capture Block Diagram
Page 133 of datasheet

## Slide 4: How to Configure ICx Pin
Tabel 10-2 (Page 108 of datasheet)
Register 10-5 (Page 113 of datasheet)

## Slide 5: ICxCON Register
Important Bits:
ICTMR
ICI
ICM
Page 134 of datasheet for details.

## Slide 6: Input Capture Event Modes
1. Simple Capture Event modes:
  Capture timer value on every falling edge of input at ICx pin
  Capture timer value on every rising edge of input at ICx pin
2. Capture timer value on every edge (rising and falling).
3. Prescaler Capture Event modes:
  Capture timer value on every 4th rising edge of input at ICx pin
  Capture timer value on every 16th rising edge of input at ICx pin

## Slide 7: Simple Capture Events
ICM = ‘011’ (every rising edge)
ICM = ‘010’ (every falling edge)
Prescaler won’t be used.

## Slide 8: Simple Capture Events
The input capture logic detects and synchronizes the rising or falling edge of the capture pin signal on the internal instruction clock. If the rising/falling edge has occurred, the capture module logic will write the current timer value to the capture buffer and will trigger the interrupt generation logic when the number of elapsed capture events matches the number specified by the ICI control bits (ICI1:ICI0) in the ICxCON1 register (ICxCON1<6:5>), and the respective Input Capture Interrupt Flag, ICxIF, is asserted two instruction cycles after the capture buffer write event.
If the capture timer increments every instruction cycle, the captured timer value will be the value that was present one or two instruction cycles after the time of the event on the ICx pin.

## Slide 9: Prescaler Capture Events
ICM = ‘100’ (every 4th rising edge)
ICM = ‘101’ (every 16th rising edge)

## Slide 10: Edge Detection Mode
ICM = ‘001’
When Input Capture is in this mode:
  Prescaler Capture will not be used.
  The interrupt for Capture mode bits ICI will not be used.
  Set the Input Capture Interrupt Flag (ICxIF) on every edge; both rising and falling.

## Slide 11: Edge Detection Mode

## Slide 12: Question
What is the difference between ICI and ICM in the ICxCON register?

## Slide 13: Example
Measure the duty cycle of an external signal. Set RB0 to ‘1’ is the duty cycle is greater than 50%. (ic_dutyCycle.c)

## Slide 14: Quiz
Use Input Capture 2 (associated with RP3) to implement a frequency counter. Store the results using W3.

## Slide 15: Output Compare
Pulse Generation
Digital Signal Generator
Servo Control
Multiple Modes
Single Output Pulse
Continues Output Pulse
Pulse-Width Modulation

## Slide 16: Output Compare Block Diagram

## Slide 17: Output Compare Registers
Each Output Compare Channel has the following registers:
OCxCON – the control register for the output compare channel
OCxR – the data register for the output compare channel
OCxRS – a secondary data register for the output compare channel

## Slide 18: Output Compare Control Register
Page 139 of datasheet

## Slide 19: Single Compare Match Mode 1 --- Output Driven High
OCM<2:0> = 0b001
Compare forces OCx pin high, initial state of pin is low.
Interrupt is generated on the single compare match event.

## Slide 20: Single Compare Match Mode 1 --- Output Driven High
Key Timing Information:
The OCx pin is driven high one instruction clock after the compare match occurs between the TMRy and the OCxR register. The OCx pin will remain high until a mode change has been made or the module is disabled.
The TMRy will count up to the value contained in the associated Period register and then reset to 0000h on the next instruction clock.
The respective Channel Interrupt Flag, OCxIF, is asserted two instruction clocks after the OCx pin is driven high.

## Slide 21: Single Compare Match Mode 2 --- Output Driven Low
OCM<2:0> = 0b010
Compare forces OCx pin low.
Initial state of pin is high.
Interrupt is generated on the single compare match event.

## Slide 22: Single Compare Match Mode 2 --- Output Driven Low
Key Timing Information:
The OCx pin is driven low one instruction clock after the compare match occurs between the TMRy and the OCxR register. The OCx pin will remain low until a mode change has been made or the module is disabled.
The TMRy will count up to the value contained in the associated Period register and then reset to 0000h on the next instruction clock.
The respective Channel Interrupt Flag, OCxIF, is asserted two instruction clocks after the OCx pin is driven low.

## Slide 23: Single Compare Match Mode 3 --- Toggle Output
OCM<2:0> = 0b011
Compare toggles OCx pin.
Toggle event is continues.
Interrupt is generated for each toggle event.

## Slide 24: Single Compare Match Mode 3 --- Toggle Output
Key Timing Information:
The OCx pin is toggled one instruction clock after the compare match occurs between the TMRy and the OCxR register. The OCx pin will remain at this new state until the next toggle event, or until a mode change has been made or the module is disabled.
The TMRy will count up to the value contained in the associated Period register and then reset to 0000h on the next instruction clock.
The respective Channel Interrupt Flag, OCxIF, is asserted two instruction clocks after the OCx pin is toggled.

## Slide 25: Single Compare Match Mode 3 --- Toggle Output
Key Timing Information:
In this example, note that OCxR == PRy.

## Slide 26: Single Compare Match Mode 3 --- Toggle Output
Toggle Mode Initial State Setup

## Slide 27: Single Compare Match Mode 3 --- Toggle Output
Toggle Interrupt Servicing

## Slide 28: Reading Assignment
PIC24F Family Reference Manual Section 16. Output Compare (Advance Information, posted on Moodle site)