## Slide 1: EE 2361: Introduction to Microcontrollers
Peng Li
lipeng@umn.edu
07/13/2015

## Slide 2: Topics
Output Compare Dual Compare Match Mode
Pulse Width Modulation (PWM) Mode

## Slide 3: Dual Compare Match Mode
OCM<2:0> = 0b100 or 0b101
In this mode, the module uses both the OCxR and OCxRS registers for the compare match events.
The OCxR register is compared against the incrementing timer count, TMRy, and the leading (rising) edge of the pulse is generated at the OCx pin, on a compare match event.
The OCxRS register is then compared to the same incrementing timer count, TMRy, and the trailing (falling) edge of the pulse is generated at the OCx pin, on a compare match event.

## Slide 4: Dual Compare Match Mode --- Single Output Pulse
OCM<2:0> = 0b100

## Slide 5: Dual Compare Match Mode --- Single Output Pulse
Sample Codes

## Slide 6: Dual Compare Match Mode --- Continuous Output Pulse Mode
OCM<2:0> = 0b101

## Slide 7: Dual Compare Match Mode --- Continuous Output Pulse Mode
Sample Codes

## Slide 8: Example
oc_contPulses.c
oc_siren.c
Logic Analyzer in MPLAB

## Slide 9: Exercise
Generate an output signal with the following configuration:
Frequency = 1MHz.
Duty Cycle = 12.5%.
Using Timer 2, which will use the 16MHz instruction clock cycle.
How do you initialize Timer 2 (T2CON, PR2) and Output Compare module 1 (OC1CON, OC1R, OC1RS)?

## Slide 10: Simple Pulse-Width Modulation (PWM) Mode
OCM<2:0> = 0b110
Set the PWM period by writing to the selected Timer Period Register (PRy).
Set the PWM duty cycle by writing to the OCxRS register.
OCxR register will load the value stored in OCxRS register.

## Slide 11: PWM Mode Output Wave Form

## Slide 12: PWM Period

## Slide 13: PWM Duty Cycle
Specified by writing to the OCxRS register.
It can be written at any time.
However, the duty cycle value is not loaded into OCxR until a match between Pry and TMRy happens.

## Slide 14: PWM Duty Cycle
If the duty cycle register, OCxR, is loaded with 0000h, the OCx pin will remain low (0% duty cycle).
If OCxR is greater than PRy (Timer Period register), the pin will remain high (100% duty cycle).
If OCxR is equal to PRy, the OCx pin will be low for one time base count value and high for all other count values.

## Slide 15: OCxRS = 0

## Slide 16: OCxRS > PRy

## Slide 17: OCxRS = PRy

## Slide 18: 0 < OCxRS < PRy

## Slide 19: Coding Example for PWM Setup
Question: what is the duty cycle and frequency of the PWM signal?

## Slide 20: Exercise
Use the output compare module and polling to generate a signal that has the following properties: (1) its rising edges are 1ms apart. (2) the signal goes through a cycle in which the high pulse width increases from 0.1ms, to 0.9ms with increments of 0.2ms.