## Slide 1: EE 2361: Introduction to Microcontrollers
Peng Li
lipeng@umn.edu
07/15/2015

## Slide 2: Topics
Coding Example for PWM
UART

## Slide 3: PWM Example (oc_varPwm.c)
Goal: Use the output compare module and polling to generate a signal that has the following properties: (1) its rising edges are 4us apart. (2) the signal goes through a cycle in which the high pulse width increases from 1us, to 3us with increments of 1us.
Method: use Output Compare PWM mode in a loop.
Calculations: Period = 4us, so PR2 = 63 High Pulse = 1us, Duty Cycle = 25%, OC1RS = (PR2 + 1) * Duty Cycle = 16. High Pulse = 2us, Duty Cycle = 50%, OC1RS = (PR2 + 1) * Duty Cycle = 32. High Pulse = 3us, Duty Cycle = 75%, OC1RS = (PR2 + 1) * Duty Cycle = 48.
Use Window > Simulator > Analyzer to see the output.

## Slide 4: Data Communication Between Devices
Chip to chip (other microcontroller)
Chip to computer (chip)
UART: Universal Asynchronous Receiver Transmitter.
One of the serial communication method.

## Slide 5: How UART Works
Chip A
Chip B
TX
RX
RX
TX
01000111
1010010

## Slide 6: Full Duplex vs. Half Duplex
Chip A
Chip B
TX
RX
RX
TX
01000111
Half Duplex:
Only a single wire is available.
Receiving and transmitting a data frame cannot happen at the same time. They will have to share the data link.

## Slide 7: Full Duplex vs. Half Duplex
Chip A
Chip B
TX
RX
RX
TX
01000111
1010010
Full Duplex:
One wire for each direction.
Receiving and transmitting a data frame can happen at the same time.
PIC24

## Slide 8: Data Frame
Chip A
Chip B
TX
RX
RX
TX
Data is transmitted/received frame by frame.
DataFrame1
DataFrame2
…
……
DataFrame8
DataFrame7

## Slide 9: Data Frame
What Data Frame Looks Like:
1 Start Bit + 8 Data Bits + (1 Parity Bit) + 1 Stop Bit
Optional
‘0’
‘1’

## Slide 10: Parity Bit
For Error Detection, but it is optional.
If it is enabled, we have two options. Even Parity or Odd Parity.
Even Parity: If the number of ‘1’ in the data bits is an even number, set this bit to 0. Otherwise, set it to 1.
Odd Parity: If the number of ‘1’ in the data bits is an odd number, set this bit to 1. Otherwise, set it to 0.

## Slide 11: Parity Bit Example
8 Data Bits | Number of 1s | Even Parity | Odd Parity
01011011 | 5 | 010110111 | 010110110
01010101 | 4 | 010101010 | 010101011
00000000 | 0 | 000000000 | 000000001
11111111 | 8 | 111111110 | 111111111
Even Parity Bit = (# of 1s) (mod 2)
Odd Parity Bit = (# of 1s + 1) (mod 2)

## Slide 12: Baud Rate
Number of pulses (bits) per second.
Example: 1 kBd = 1000 Bd = 1000 pulses (bits) per second. Each pulse takes 0.1ms.
To be able to transfer date between receiver and transmitter. Both need to have the same data frame format and Baud Rate.

## Slide 13: PIC24F UART
Full-Duplex, 8 or 9-bit Data Transmission.
Even, Odd or No Parity Options.
One or Two Stop Bits.
Baud Rates Ranging from 1Mbps to 15 bps at 16 MHz instruction clock frequency.
Transmit and Receive Interrupts.
Two UART modules.

## Slide 14: UART Baud Rate Generator
UxBRG register controls the period of the UART Baud Rate.
Question: Given that Fcy = 16MHz, what is the maximum and minimum Baud Rate that can be generated?

## Slide 15: Baud Rate Table

## Slide 16: Baud Rate Error Calculation
Error = (Calculated Baud Rate – Desired Baud Rate) / Desired Baud Rate

## Slide 17: UART Configuration
One Start bit + eight or nine data bits + one or two Stop bits.
Most Common Format (default setting): One Start bit + 8 Data bits (no parity) + one Stop bit.

## Slide 18: UART Control Register (UxMODE)
PDSEL<1:0> - Number of data bits.
11 = 9-bit data, no parity
10 = 8-bit data, even parity
01 = 8-bit data, odd parity
00 = 8-bit data, no parity
STSEL - Number of Stop bits.
1 = 2 Stop bits
0 = 1 Stop bit.
UARTEN – Enable/Disable UART
1 = Enable
0 = Disable

## Slide 19: UART Status and Control Register (UxSTA)
UAXEN – Transmit Enable/Disable bit
1 = Transmit Enable
0 = Transmit Disable

## Slide 20: UART Transmit Register (UxTXREG)

## Slide 21: UART Receive Register (UxRXREG)