## Slide 1
Chapter 4: Differential Amplifiers
4.1 Single-Ended and Differential Operation
4.2 Basic Differential Pair
4.3 Common-Mode Response
4.4 Differential Pair with MOS Loads
4.5 Gilbert Cell

## Slide 2: Single-Ended and Differential Operation
A “single-ended” signal is one that is measured with respect to a fixed potential, usually the ground [Fig. (a)]
A differential signal is one that is measured between two nodes that have equal and opposite signal excursions around a fixed potential [Fig. (b)]
The “center” potential in differential signaling is called the “common-mode” (CM) level
  bias value of the voltages, i.e., value in the absence of signals

## Slide 3: Single-Ended and Differential Operation
Suppose each single-ended output in Fig. (b) has a peak amplitude of V0
Then single-ended peak-to-peak swing is 2V0 and differential peak-to-peak swing is 4V0
For example, if voltage at X (w.r.t. ground) is V0cosωt + VCM and that at Y is -V0cosωt + VCM, then the peak-to-peak swing of VX - VY is 4V0

## Slide 4: Advantages of Differential Operation
Higher immunity to “environmental” noise in differential operation as compared to single-ended signaling
In Fig. (a), transitions on the clock line L2 corrupt the signal on sensitive signal line L1 due to capacitive coupling between the lines
If the sensitive signal is distributed as two equal and opposite phases as in Fig. (b), the clock line placed midway disturbs the differential phases equally and keeps the difference intact, called common-mode (CM) rejection

## Slide 5: Advantages of Differential Operation
CM rejection also occurs with noisy supply voltages
In the CS stage of Fig. (a), if VDD varies by ΔV, then Vout changes by roughly the same amount, i.e., output is susceptible to noise on VDD
In the symmetric circuit of Fig. (b), noise on VDD affects VX and VY, but not VX – VY = Vout
The differential circuit is more robust to supply noise than its single-ended counterpart

## Slide 6: Advantages of Differential Operation
Differential operation is as beneficial for sensitive signals (“victims”) as for noisy lines (“aggressors”)
Clock signal is distributed in differential form on two lines
With perfect symmetry, the components coupled from CK and C̅K to the signal line cancel each other

## Slide 7: Advantages of Differential Operation
Differential signaling increases maximum achievable voltage swings
In the above differential circuit, the maximum output swing at X or Y is equal to VDD – (VGS – VTH)
For VX – VY, the maximum swing is 2[VDD – (VGS – VTH)]
Other advantages of differential circuits include simpler biasing and higher linearity
Advantages of differential operation outweigh the possible increase in area

## Slide 8: Basic Differential Pair: Introduction
The simple differential circuit shown incorporates two identical single-ended paths to process the two phases
The two differential inputs Vin1 and Vin2, having a certain CM level Vin,CM are applied to the gates
The outputs are differential too and swing around the output CM level Vout,CM
This circuit offers all advantages of differential signaling: supply noise rejection, higher output swings, etc.

## Slide 9: Basic Differential Pair: Introduction
As the input CM level, Vin,CM changes, so do the bias currents of M1 and M2, thus varying both the transconductance of the devices and the output CM level
As shown in Fig. (b), if the input CM level is excessively low, the minimum values of Vin1 and Vin2 may turn off M1 and M2, leading to severe clipping at the output
Bias currents of the devices should have minimal dependence on the input CM level

## Slide 10: Basic Differential Pair
A “differential pair” incorporates a current source ISS to make ID1 + ID2 independent of Vin,CM
If Vin1 = Vin2, the bias current of both M1 and M2 is ISS/2 and the output CM level is VDD – RDISS/2

## Slide 11: Basic Differential Pair: Qualitative Analysis
When Vin1 is much more negative than Vin2, M1 is off, M2 is on and ID2 = ISS, Vout1 = VDD and Vout2=VDD – RDISS
As Vin1 is brought closer to Vin2, M1 gradually turns on, drawing a fraction of ISS from RD1 and lowering Vout1
Since ID1 + ID2 = ISS, ID2 falls and Vout2 rises
For Vin1=Vin2, Vout1=Vout2=VDD – RDISS/2, which is the output CM level
When Vin1 becomes more positive than Vin2, ID1 becomes higher than ID2 and Vout1 drops below Vout2
For sufficiently large Vin1 – Vin2, M1 “hogs” all of ISS, turning M2 off, therefore, Vout1 = VDD – RDISS and Vout2 = VDD

## Slide 12: Basic Differential Pair: Qualitative Analysis
The circuit contains three differential quantities: Vin1 – Vin2, Vout1 – Vout2, and ID1 – ID2
The maximum and minimum levels at the output are well-defined and independent of the input CM level
The small-signal gain (slope of Vout1 – Vout2 versus Vin1 – Vin2) is maximum for Vin1 = Vin2 and gradually falls to zero as |Vin1 – Vin2| increases
Circuit becomes more nonlinear as input voltage swing increases
For Vin1 = Vin2, circuit is said to be in “equilibrium”

## Slide 13: Basic Differential Pair: Common-mode behavior
Tail current source suppresses the effect of input CM level variations on the output level
Set Vin1 = Vin2 = Vin,CM and vary Vin,CM from 0 to VDD [Fig. (a)]
Due to symmetry, Vout1 = Vout2
For Vin,CM = 0, M1 and M2 are off, ID3 = 0 and M3 operates in the deep triode region [Fig. (b)]
With ID1 = ID2 = 0, circuit is incapable of signal amplification; Vout1 = Vout2 = VDD, and VP = 0

## Slide 14: Basic Differential Pair: Common-mode behavior
M1 and M2 turn on if Vin,CM ≥ VTH
Beyond this point, ID1 and ID2 continue to increase and VP also rises [Fig. (c)]
M1 and M2 act as a source follower, forcing VP to follow Vin,CM
When Vin,CM is sufficiently high, VDS3 exceeds VGS3 – VTH3, and M3 operates in saturation so that ID1+ID2 is constant
For proper operation, Vin,CM ≥ VGS1 + (VGS3 – VTH3)

## Slide 15: Basic Differential Pair: Common-mode behavior
As Vin,CM rises further, Vout1 and Vout2 stay relatively constant, therefore, M1 and M2 enter the triode region if Vin,CM > Vout1 + VTH = VDD – RDISS/2 + VTH
The allowable value of Vin,CM is bounded as follows:
Beyond the upper bound, the CM characteristics of Fig. (c) do not change, but the differential gain drops

## Slide 16: Basic Differential Pair: Output Swings
Suppose the input and output bias levels are Vin,CM and Vout,CM respectively, and Vin,CM < Vout,CM
Assume a high voltage gain so that input swing is much lesser than the output swing
For M1 and M2 to remain saturated, each output can go as high as VDD and as low as Vin,CM – VTH
Vin,CM can be no less than VGS1 + (VGS3 – VTH3)
With this choice of Vin,CM, single-ended peak-to-peak swing is VDD – (VGS1 – VTH1) – (VGS3 – VTH3)

## Slide 17: Basic Differential Pair: Large-signal Analysis
Objective is to determine Vout1 – Vout2 as a function of Vin1 – Vin2
If RD1 = RD2 = RD, we have
Assume the circuit is symmetric, M1 and M2 are saturated and λ = 0
Since VP = Vin1 – VGS1 = Vin2 – VGS2 , Vin1 – Vin2 = VGS1 – VGS2
For a square-law device,
Therefore,

## Slide 18: Basic Differential Pair: Large-signal Analysis
It follows from previous derivation that
To find ID1 – ID2, square both sides of above eqn., and recognize that ID1 + ID2 = ISS
Thus,
Squaring both sides and noting that 4ID1ID2 = (ID1 + ID2)2 – (ID1 – ID2)2, we arrive at

## Slide 19: Basic Differential Pair: Large-signal Analysis
Thus
ID1 – ID2 is an odd function of Vin1 – Vin2, falling to zero for Vin1 = Vin2
As |Vin1 – Vin2| increases from zero, |ID1 – ID2| increases
To find the equivalent Gm of M1 and M2, denote ID1 – ID2 and Vin1 – Vin2 as ΔID and ΔVin respectively
It can be shown that

## Slide 20: Basic Differential Pair: Large-signal Analysis
For ΔVin = 0, Gm is maximum and equal to
Since Vout1 – Vout2 = RDΔID = -RDGmΔVin , small-signal differential voltage gain in equilibrium condition is
Since each transistor carries ISS/2 in equilibrium, the factor is the same as gm, i.e., |AV|=gmRD
Previous result suggests that Gm falls to zero for
As ΔVin exceeds a limit ΔVin1, one transistor carries the entire ISS, turning off the other
For this ΔVin, ID1 = ISS, and ΔVin1 = VGS1 – VTH since M2 is nearly off, thus

## Slide 21: Basic Differential Pair: Large-signal Analysis
For ΔVin > ΔVin1, M2 is off and the equation derived for ΔID no longer holds [Fig. (a)]
Gm is maximum for ΔVin = 0 and falls to zero for ΔVin = ΔVin1 [Fig. (b)]

## Slide 22: Basic Differential Pair: Large-signal Analysis
As W/L increases, ΔVin1 decreases, narrowing the input range across which both devices are on [Fig. (b)]
As ISS increases, both the input range and the output current swing increase [Fig. (c)]
Intuitively, circuit becomes more linear as ISS increases or W/L decreases

## Slide 23: Basic Differential Pair: Large-signal Analysis
ΔVin1 represents the maximum differential input the circuit can “handle”
ΔVin1 can be tied to the overdrive voltage of M1 and M2 in equilibrium
For zero differential input, ID1 = ID2 = ISS/2, yielding
Thus, ΔVin1 is equal to √2 times the equilibrium overdrive
Increasing ΔVin1 to improve linearity increases overdrive of M1 and M2, which for a given ISS is achieved only by decreasing W/L and hence gm, thereby reducing differential gain
Alternatively, ISS can be increased but with higher power consumption

## Slide 24: Basic Differential Pair: Small-signal Analysis
Assume M1 and M2 are saturated and apply small-signal inputs Vin1 and Vin2
The differential gain (Vout1 – Vout2)/(Vin1 – Vin2) was found to be from large-signal analysis
Since each transistor carries approximately ISS/2 current in the vicinity of equilibrium, this expression reduces to gmRD
Assume RD1 = RD2 = RD, the small-signal analysis is carried out using two methods

## Slide 25: Basic Differential Pair: Small-signal Analysis (I)
Method 1: Superposition
First set Vin2 = 0 and find the effect of Vin1 at X and Y
To find VX, note that M1 forms a CS stage with a degeneration resistance equal to the impedance looking into the source of M2, RS = 1/gm2, neglecting channel-length modulation and body effect [Fig. (b)]
Then from Fig. (c),

## Slide 26: Basic Differential Pair: Small-signal Analysis (I)
Method 1: Superposition
To find VY, we note that M1 drives M2 as a source follower and replace Vin1 and M1 by its Thevenin equivalent
Thevenin voltage VT = Vin1, and resistance RT = 1/gm1
M2 operates as a common-gate stage, with a gain

## Slide 27: Basic Differential Pair: Small-signal Analysis (I)
From previous analysis, the overall voltage gain for Vin1 is
For gm1 = gm2 = gm, this reduces to
By symmetry, the effect of Vin2 at X and Y is identical to that of Vin1 with reverse polarities
Adding the two results to perform superposition,
Magnitude of gain is gmRD regardless of how inputs are applied, halved for single-ended output

## Slide 28: Half-Circuit Lemma/Concept
D1 and D2 represent any three-terminal active device in a symmetric circuit
Assume Vin1 and Vin2 change differentially, from V0 to V0 + ΔVin and from V0 to V0 – ΔVin respectively
If the circuit remains linear, VP does not change (acts as a virtual or ac ground)
This is referred to as the “half-circuit concept”

## Slide 29: Basic Differential Pair: Small-signal Analysis (II)
Using the half-circuit concept, VP experiences no change node P can be considered “ac ground” or virtual ground and the circuit can be decomposed into two separate halves
We can write and
Vin1 and –Vin1 represent the voltage change on each side
Thus, , same result as in Method 1

## Slide 30: Half-Circuit Technique
The half-circuit technique can be applied even if the two inputs are not fully differential
The unsymmetrical inputs Vin1 and Vin2 each can be viewed as the sum of a differential component and a common-mode component, as

## Slide 31: Half-Circuit Technique
The circuit can be visualized as shown above
The circuit senses a combination of a differential input and a common-mode variation
Effect of each type of input can be computed by superposition, with the half-circuit applied to the differential-mode operation

## Slide 32: Half-Circuit Technique: Example
Unsymmetrical inputs Vin1 and Vin2 are superposed as differential [Fig. (a)] and common-mode [Fig. (b)] signals

## Slide 33: Half-Circuit Technique: Example
For differential-mode operation, circuit reduces to Fig. (a)
Thus,

## Slide 34: Half-Circuit Technique: Example
For common-mode operation, circuit reduces to that in Fig. (b)
If circuit is fully symmetric and ISS is an ideal current source, the currents drawn by M1 and M2 from RD1 and RD2 are exactly equal to ISS/2 and independent of Vin,CM
VX and VY remain equal to VDD – RD(ISS/2) and do not vary with Vin,CM, therefore, circuit simply amplifies Vin1 – Vin2 while eliminating the effect Vin,CM

## Slide 35: Degenerated Differential Pair
A differential pair can incorporate resistive degeneration to improve linearity [Fig. (a)]
RS1 and RS2 soften the nonlinear behavior of M1 and M2 by increasing the differential voltage necessary to turn off one side [Fig. (b)]
Suppose at Vin1 – Vin2 = ΔVin2, M2 turns off and ID1 = ISS, then VGS2 = VTH and hence

## Slide 36: Degenerated Differential Pair
Thus
First term on RHS is ΔVin1, the input difference needed to turn off M2 if RS = 0, giving
Linear input range is widened by approximately ±RSISS

## Slide 37: Degenerated Differential Pair
The small-signal voltage gain can be found using the half-circuit concept
The half-circuit is simply a degenerated CS stage exhibiting a gain of
if λ = γ = 0
The degenerated circuit trades gain for linearity
AV is less sensitive to gm variations

## Slide 38: Degenerated Differential Pair
Degeneration resistors consume voltage headroom
In equilibrium, each resistor sustains a voltage drop of RSISS/2 and maximum allowable differential swing is reduced by RSISS/2
This can be resolved by splitting the tail current source in half and connecting each to the source terminal
No headroom is sacrificed across the degeneration resistance in equilibrium

## Slide 39: Basic Differential Pair: Common-Mode Response
In reality, the differential pair is not fully symmetric and the tail current source exhibits a finite output impedance
A fraction of the input CM variations appear at the output
First assume that circuit is symmetric but tail current source has a finite output impedance RSS [Fig. (a)]
Increase in Vin,CM causes VP to increase and both VX, VY to drop, which remain equal due to symmetry [Fig. (b)]

## Slide 40: Basic Differential Pair: Common-Mode Response
M1 and M2 are “in parallel” and can be reduced to one composite device with twice the width, bias current and transconductance
“Common-mode gain” of the circuit is (λ = γ = 0)
Input CM variations disturb bias points and affect small-signal gain and output swings

## Slide 41: Basic Differential Pair: Common-Mode Response
There is variation in differential output due to change in Vin,CM since the circuit is not fully symmetric, i.e., slight mismatches between the two sides
RD1 = RD, RD2 = RD + ΔRD, where ΔRD denotes a small mismatch and circuit is otherwise symmetric (λ = γ = 0 for M1 and M2)
M1 and M2 operate as one source follower, raising VP by

## Slide 42: Basic Differential Pair: Common-Mode Response
Since M1 and M2 are identical, ID1 and ID2 increase by
VX and VY change by different amounts
Common-mode change at the input introduces a differential component at the output – common-mode to differential conversion

## Slide 43: Basic Differential Pair: Common-Mode Response
Common-mode response depends on output impedance of tail current source and asymmetries in the circuit
Two effects:
  Variation of output CM level (in the absence of mismatches)
  Conversion of input CM variations to output differential components (more severe)

## Slide 44: Common-mode to differential conversion
CM to differential conversions become significant at high frequencies since the total capacitance shunting the tail current source introduces larger tail current variations
This capacitance is arises from parasitics of the current source and source-bulk junctions of M1 and M2
Asymmetry in the circuit stems from both the load resistors and the input transistors
  Latter contributes a greater mismatch

## Slide 45: Common-Mode Response: Transistor Mismatch
M1 and M2 exhibit unequal transconductances gm1 and gm2 due to dimension and VTH mismatches (assume λ = γ = 0)
Calculate small-signal gain from Vin,CM to X and Y [Fig. (b)]
Also,

## Slide 46: Common-Mode Response: Transistor Mismatch
Thus,
We now obtain the output voltages as
The differential component at the output is

## Slide 47: Common-Mode Response: Transistor Mismatch
The circuit converts input CM variations to a differential error by a factor of
ACM-DM denotes common-mode to differential-mode conversion and Δgm = gm1 – gm2

## Slide 48: Common-Mode Response
Common-mode rejection ratio (CMRR) is defined as the desired gain divided by undesired gain
If only gm mismatch is considered, it can be shown that
Hence,
gm denotes the mean value, i.e., gm = (gm1 + gm2)/2
2gmRSS >> 1 and hence

## Slide 49: Differential Pair with MOS Loads
Differential pairs can employ diode-connected [Fig. (a)] or current-source loads [Fig. (b)]
For Fig. (a), small-signal differential gain is
N and P subscripts denote NMOS and PMOS respectively

## Slide 50: Differential Pair with MOS Loads
Expressing gmN and gmP in terms of device dimensions,
For current-source loads [Fig. (b)], the gain is

## Slide 51: Differential Pair with MOS Loads
Diode-connected loads consume voltage headroom and create trade-off between output voltage swing, input CM range and gain
For higher gain, (W/L)P must decrease, thereby increasing |VGS – VTHP| and lowering output CM level
Solved by adding PMOS current sources M5 and M6 to supply part of input pair bias current [Fig. (a)]

## Slide 52: Differential Pair with MOS Loads
In Fig. (a), gm of load devices M3 and M4 is lowered by reducing their current instead of (W/L)P
For ID5 = ID6 = 0.8ID1 = 0.8ID2, ID3 and ID4 are reduced by a factor of 5
For a given overdrive, gmP is lowered by the same factor
Differential gain is five times that of the case without auxiliary PMOS current sources (if λ = 0)

## Slide 53: Differential Pair with MOS Loads
Since diode-connected loads limit output swings, loads are realized by resistors
Maximum voltage at each output node is VDD - |VGS3,4 – VTH3,4| instead of VDD - |VTH3,4| for diode-connected loads
For a given output CM level and 80% auxiliary currents, RD can be five times larger, yielding a voltage gain of

## Slide 54: Cascode Differential Pair
Small-signal voltage gain can be increased by increasing output impedance of both NMOS and PMOS devices via cascoding [Fig. (a)], but at the cost of less headroom
The gain is calculated using the half-circuit technique [Fig. (b)]

## Slide 55: Gilbert Cell
Differential pair whose gain is controlled by a control voltage [Fig. (a)]
In Fig.(a), the control voltage Vcont controls the tail current and hence the gain
Here, Av = Vout/ Vin varies from zero (if ID3 = 0)to a maximum value given by voltage headroom limitations and device dimensions
Simple example of Variable Gain Amplifier (VGA)

## Slide 56: Gilbert Cell
An amplifier is sought whose gain can be continuously varied from a negative to a positive value
Fig. (b) shows two differential pairs that amplify the input by opposite gains
Here, Vout1/Vin = -gmRD and Vout2/Vin = +gmRD
If I1 and I2 vary in opposite directions, so do |Vout1/Vin| and |Vout2/Vin|

## Slide 57: Gilbert Cell
Vout1 and Vout2 are combined into a single output as shown in Fig. (a)
The two voltages are summed , producing Vout = Vout1 + Vout2 = A1Vin + A2Vin, where A1 and A2 are controlled by Vcont1 and Vcont2 respectively
Actual implementation shown in Fig. (b) where drain terminals are shorted to sum the currents and generate the output voltage

## Slide 58: Gilbert Cell
Vout1 and Vout2 must change I1 and I2 in opposite directions so that the amplifier gain changes monotonically
This is done using a differential pair, as shown in Fig. (c)
For large |Vcont1 – Vcont2|, all of ISS is steered to one of the top differential pairs and |Vout/Vin| is maximum
If Vcont1 = Vcont2, the gain is zero
Simplified structure in Fig.(d), called a “Gilbert Cell”